## Slide 1: Introduction
A digital computer stores values using the binary number system, where a number is represented by a string of 0's and 1's. Each binary digit is termed a bit.
Digital computers have a finite bit capacity (memory), so integers and real numbers are represented by a fixed number of binary bits.
  Integers can be represented exactly as long as the integer value falls within the fixed number of bits.
  Floating point numbers such as 2.67 cannot be represented exactly.
We will develop storage systems for both integers and floating point numbers and see the advantages and disadvantages of these systems.
Truncation errors occur when functions such as sin(x) must be evaluated by the partial sum of an infinite series.

## Slide 2: Nonnegative Integer Representation
Suppose that p bits are available to represent an integer. A positive integer has a zero in the last bit and the p - 1 other bits contain the base-2 representation of the integer.
  For example, if p = 8

## Slide 3: Negative Integer Representation

## Slide 4: Example 1

## Slide 5: Twos Complement

## Slide 6: Twos Complement and the Carry Bit
If we add 1 and -1 the result must be 0. 00000001 + 11111111 = 1 | 00000000 Discard the carry and the result is 0.
Carry

## Slide 7: Twos Complement and the Carry Bit
Another example:

## Slide 8: Example 2
Find the representation for -7 7 00000111 -7 11111000 + 1 = 11111001
Find the representation for -100 100 01100100 -100 10011011 + 1 = 10011100

## Slide 9: Performing Twos Complement Addition and Subtraction
Given two p-bit integers m and n , form m + n by performing binary addition and discarding the carry.
The subtraction m-n is performed adding ( -n ) to m , so m – n = m + 2comp(n).

## Slide 10: Integer Range
With p binary bits, the range is

## Slide 11: Integer Overflow
There are only p bits to work with, 1/2 nonnegative and 1/ 2 negative. Overflow can occur.
0 | 0 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
+
1 | 0 | 0 | 0 | 0 | 1 | 1 | 1
=
-121
NOTE: Overflow has occurred when the sign bit is the opposite of what it should be.

## Slide 12: Example 3
Assume b = 2 and p = 12.
  The range of integers that can be represented is
  Show that overflow occurs when computing 1870 + 675 011101001110 + = 100111110001 = - 1551 001010100011

## Slide 13: Floating-Point Representation
For given integers b, p, nmin , and nmax , the floating-point numbers are real numbers of the form
with and .
    b is the base. The most common bases are b=2 (binary base), b=10 (decimal base), and b=16 (hexadecimal base).
    n is the exponent that defines the order of magnitude of the number to be encoded.
    The integers are called the digits and p is the number of significant digits. The mantissa is the integer .

## Slide 14: Floating-Point Representation
The smallest and largest floating-point numbers in magnitude are
Smaller numbers cause underflow, and larger numbers cause overflow.
Computers usually support single precision (i.e., representation with 32 bits) and double precision (i.e., representation with 64 bits). In our single-precision representation, 1 bit is used for the sign, 8 bits for the exponent, and 23 bits for the mantissa (for a total of 32 bits).

## Slide 15: Floating-Point Representation
The exponent is encoded as an unsigned number by adding to it a "bias" (127 is the usual bias in single precision). Using this notation we write 81.625 as The exponent is , and 81.625 is stored as follows:
0 | 10000110 | 10100011010000000000000
7+127 = 134 = 100001102

## Slide 16: Exponent Range Accounting for the Bias
Bias 127 notation, 8-bit exponent
  Stored exponent = actual exponent + 127
    Stored exponent = 0, actual exponent = -127
    Stored exponent = 111111112 = 28-1 = 255 Actual exponent = 255-127 = 128
Actual exponent range: .

## Slide 17: Example 4
Find the 32-bit single precision representation for -23.5625.
5 + 127 = 132 = 100001002
Floating point representation: 1|10000100|10111100100000000000000
sign
exponent
mantissa

## Slide 18: Example 5
Find the floating point representation of
0.0390625
Exponent = 127+ (-4) = 123 = 11110112
Floating point representation: 0|01111011|10100000000000000000000
sign
exponent
mantissa

## Slide 19: Rounding and Truncation
NOTE: Rounding is preferred.

## Slide 20: fl(x)

## Slide 21: IEEE Format
The most widely used standard for floating-point computation is the IEEE Standard for Floating-Point Arithmetic.
  A nonzero number is assumed to have a hidden 1 prior to the first digit of the mantissa.
  Single precision uses 24 binary digits, and double precision 53.

## Slide 22: IEEE Format
The table lists the properties of single and double precision IEEE floating point.

## Slide 23: Granularity of Floating Point
Floating point numbers are granular, which means there are gaps between numbers. The granularity is caused by the fact that a finite number of bits are used to represent a floating point number.
  Most real numbers must be approximated because there is no exact conversion into binary.

## Slide 24: Granularity of Floating Point
The distance from 1.0 to the next largest double-precision number is 2-52 in IEEE double precision, and this is called the machine precision, or eps.
  If a number smaller than 2-52 is added to 1, the result will be 1.
  The floating point numbers between 1.0 and 2.0 are equally spaced:

## Slide 25: Granularity of Floating Point
The gap increases as the length of intervals become larger by a factor of 2. The numbers between 2.0 and 4.0 are separated by a gap of 2-51.
In general, an interval from 2k to 2k+1 has a gap between values of 2k(2-52). As k increases, the gap relative to 2k remains 2-52.

## Slide 26: General Machine Precision
If b = 2 and p = 52, eps = (1/2)2-51 = 2-52.
If b = 2 and p = 23, eps = (1/2)2-22 = 2-23.

## Slide 27: Example 6
If b = 2 and p = 25, what is the machine precision?

## Slide 28: IEEE Double Precision Range

## Slide 29: Floating-Point Accuracy
The mapping from real number to floating-point numbers is called the floating-point representation or rounding.
Let fl(x)be the floating-point number associated with the real number x. The following equality holds for all real numbers : where .

## Slide 30: Floating-Point Accuracy
To analyze accuracy of floating point operations, just consider "+".
  Let be the computer result of floating point addition.
Overflow
Underflow
NOTE: Similar notation applies for the other operations .

## Slide 31: The Guard Digit

## Slide 32: Ways of Measuring Error
Absolute error:
Relative error:

## Slide 33: Measuring Relative Error is Best
Relative error gives an indication of how good a measurement is relative to the size of the thing being measured.

## Slide 34: Measuring Relative Error is Best
This is particularly true for large or small floating point values.

## Slide 35: Measuring Relative Error is Best
Relative error is generally the better measure of truncation error when summing a series. If sn and sn+1 are the last two partial sums, estimate the relative error using where tol is the error tolerance.

## Slide 36: MATLAB Example
Approximate the sum of the series
tol = 1.0e-12;
estrelerror = inf;
sn = 0.5;
i = 2;
while estrelerror >= tol
sn_plus1 = sn + 1/(i^2 + sqrt(i));
estrelerror = abs(sn_plus1 - sn)/abs(sn);
sn = sn_plus1;
i = i + 1;
end
fprintf('The approximate sum of the series is %g.\n',sn);
<Output>
The approximate sum of the series is 1.04615.

## Slide 37: Rounding Error Bound for Addition
Most computer implementations of addition (including the widely used IEEE arithmetic) satisfy the property that the relative error is less than the machine precision:

## Slide 38: General Rounding Error
Once floating point numbers x and y are in computer memory, the basic arithmetic operations satisfy the following:

## Slide 39: Performing Many Floating Point Operations
The relative error for one single operation is very small, but this is not always the case when a sequence of many operations is performed.

## Slide 40: Rounding Error Bound for
When adding n floating point numbers, the result is the exact sum of the n numbers, each perturbed by a small relative error. The errors are bounded by K( n-1 )eps , where eps is the unit roundoff error and K is a constant that depends on x1, x2, …, xn.

## Slide 41: Rounding Error Bound for the Product of n Numbers
The relative error in computing the product of n floating point numbers is at most 1.06( n-1 )eps , assuming that ( n-1 )eps < 0.1 .

## Slide 42: Matrix Error Bounds
For an m × n matrix M define ; that is is the matrix whose entries are the absolute value of those from M. Let A and B be two floating point matrices and c be a floating point number. Then,
If the product of A and B is defined,

## Slide 43: Organizing Computations to Minimize Round Off Error
Often, carefully choosing the order in which computations are performed will improve results.

## Slide 44: Organizing Computations to Minimize Round Off Error
Consider computing the 2-norm of a vector. If some xi is too large, overflow can occur in computing the sum. There is a way to minimize errors.

## Slide 45: Organizing Computations to Minimize Round Off Error
To compute the 2-norm without the possibility of overflow, execute the following steps:

## Slide 46: Cancellation Error
Subtracting numbers that are close can be disastrous.
  Consider the quadratic formula
  If the product 4ac is small, then , ,and when computing one of x1 or x2 we will be subtracting two nearly equal numbers. This can be a serious problem, since we know a computer maintains only a fixed number of significant digits.

## Slide 47: Cancellation Error
If b > 0, cancellation error occurs when computing x1.
If b < 0, cancellation error occurs when computing x2.

## Slide 48: Cancellation Error
Fix for the quadratic equation cancellation error problem.